## Slide 1: Laser Device – EMM5
Process description
Jeroen Koldenhof

## Slide 2: Measurement Process
Get Measurements Start WS
Get Measurements End WS
Get Measurements Start DS
Get Measurements End DS
4 times same process will be handled.

## Slide 3: Get Measurement Start WS
STEP 1) Activity Operator (Laser):
  Start get thickness (laser software)
  Stop/accept get thickness (laser software)
  Start get batch info (laser software)
  Stop/accept get batch info:
    Output 1,
    Output 2,
    Output 3,
    Output 4,
Laser Get Thickness
Laser Get batch measurements
EMM5 Get Measurements
STEP 2) Activity Operator (EMM5):
  Get measurements Start WS:
    Thickness
    Batch information
STEP 3) Validation EMM5 values:
  Test Values are oke
    ACTION ???
  Test Values are not oke
    ACTION ???

## Slide 4: Get Measurement EMM5
Following data will be measured in EMM after pushing the button:
  Thickness (get measurement)
  Batch info (get batch measurement
Laser Get Thickness
Laser Get batch measurements
EMM5 Get Measurements
Following buttons needed in EMM5:
  Get Measurement Start WS
  Get Measurement Start DS
  Get Measurement End WS
  Get Measurement End DS

## Slide 5: Get Measurement detailed EMM5
Laser Get Thickness
Laser Get batch measurements
EMM5 Get Measurements
Step 1: Thickness will be measured as one measurement. EMM5 will get this by ‘get measurement’ and put this in the right field in EMM5 (thickness WS/DS/begin/end)
Step 2: The batchfile is get by EMM5, as per the example delivered during test on 17 November. The following information is stored in this batch:
  Output 1: Height of material
  Output 2: Waviness
  Output 3: Burr
  Output 4: Camber

## Slide 6: Data to store in EMM5
Laser Get Thickness
Laser Get batch measurements
EMM5 Get Measurements
Step 1: Thickness will be kept 1 on 1
Step 2:
  Output 1: Height of material
  Output 2: Waviness,
    hight must be < 3 mm
    Factor must be below 1,5% [wave height in mm / wave length in mm) * 100%]
  Output 3: Burr,
    90% -> max 0,010 mm
    10% -> max 0,020 mm
  Output 4: Camber
    Width < 250 mm -> must be < 0,5 mm
    Width > 250 mm -> must be < 0,2 mm

## Slide 7: Open Questions
Operator is doing the test with the Laser and is starting the measurement in EMM5; What is he doing with the outcome of the test result values….
Which values need to be saved in EMM5, I got from the laser:
  Thickness (once)
  Hight (batch) -> highest number?
  Waviness (batch) -> highest number?
  Burr (batch) -> highest number?
  Camber (batch) -> highest number?
Do we need to get the WAVELENGTH also? If so, please let me know how I can get this information out of the batch file
Do we need to store the WAVEFACTOR also?
Based on the Camber formule I need also the width of the sample. How do I get this? Will the operator fill this manually? In EMM5?
In one of the earlier mails I see something about thickness variation? Is this the variation between WS, DS, Start and End, or?